## Slide 1
RESCUE MAZE
ROBOT
Complete Build Guide · Component Selection · Comparisons
NAVIGATE
DETECT TILES
AVOID HAZARDS
DPS IT Fest 2026 · July 7 · Classes VIII–XII · 3 min × 2 attempts
Navigate. Locate. Rescue.

## Slide 2
COMPETITION OVERVIEW
ARENA SPECS
Tile size
30 × 30 cm
Path width
28 cm (approx.)
Wall height
Max 30 cm
Max robot size
25×25 or 27×27 cm
Time limit
3 min per attempt
Attempts
2 (best score counts)
TILE TYPES & ROBOT RESPONSE
White
Normal path tile — navigate through
Blue
Blink BLUE LED as confirmation
Black
Emit BUZZER sound — avoid zone
Silver
Checkpoint — safe restart point
PRELIMINARY ROUND
July 7, 2026 · 10 AM
Build your own maze at school
Layout shared at 8 AM same day
Blue/black tile detection only
Camera-recorded, evaluated online
FINAL ROUND
After July 10 results
Standardised tiled maze at host school
Variety of terrains and obstacles
Victim detection (letters/tags)
No external control — fully autonomous

## Slide 3
MICROCONTROLLER COMPARISON
Entry Level
Arduino Mega
ATmega2560 · 16 MHz · 8 KB RAM
5/10
CPU
16 MHz single-core
RAM
8 KB SRAM
Wi-Fi
None
Camera
Not feasible
GPIO
54 digital
Cost
₹400–600
PROS
+
Rock-solid real-time motor control
+
Beginner-friendly, huge community
+
15 PWM pins for motors + servos
CONS
-
Cannot process camera frames
-
8KB RAM too tight for maze map
-
No wireless — cable debug only
Overkill
Raspberry Pi
ARM Cortex-A · 1.5 GHz · 1-8 GB
6/10
CPU
1.5+ GHz quad-core
RAM
1–8 GB
Wi-Fi
Built-in
Camera
Full OpenCV + ML
GPIO
26 usable
Cost
₹4,000+
PROS
+
Full Linux — Python, OpenCV
+
Best for Final Round victims
+
Huge processing power
CONS
-
Linux jitter = motor drift
-
Needs Arduino for motors
-
30s boot time
-
Power hungry — big battery
Recommended
ESP32
Dual-core LX6 · 240 MHz · 520 KB
9/10
CPU
240 MHz dual-core
RAM
520 KB SRAM
Wi-Fi
Built-in + BLE
Camera
ESP32-CAM module
GPIO
34 usable pins
Cost
₹350–450
PROS
+
Dual core: motors on C0, logic on C1
+
ESP32-CAM for tile detection
+
Built-in Wi-Fi for live debug
+
Handles all sensors simultaneously
CONS
-
GPIO is 3.3V — needs level shifter
-
Cannot run full OpenCV
-
Simple colour thresholding only
+

## Slide 4
MOTOR DRIVER COMPARISON
Budget Option
L298N
Dual H-bridge · 2A · 5–35V
5/10
Max Current
2A per channel
Voltage
5–35V
Efficiency
~60%
Logic
5V only
Heat
Very high — heatsink needed
Cost
₹70–120
PROS
+
Cheapest, everywhere in India
+
Drives 2 motors per board
+
Simple wiring, tons of tutorials
CONS
-
~40% power wasted as heat
-
Drops 2–3V from motor voltage
-
5V logic — needs level shifter
-
Huge heatsink takes chassis space
RECOMMENDED
BTS7960 × 2
43A half-bridge · 5–27V · per module
9/10
Max Current
43A peak
Voltage
5–27V
Efficiency
~95%
Logic
3.3V / 5V native
Heat
Low — no heatsink
Cost
₹200–350 each
PROS
+
95% efficiency — no heat at all
+
3.3V logic = direct ESP32 connection
+
Handles 3S LiPo 12.6V easily
+
PWM per direction for smooth control
CONS
-
Larger board than TB6612
-
Needs 2 modules (one per motor)
-
Overkill current for BO motors
Compact Alt
TB6612FNG
Dual driver · 1.2A · 2.5–13.5V
6/10
Max Current
1.2A per channel
Voltage
2.5–13.5V
Efficiency
~92%
Logic
2.7–5.5V
Heat
Barely warm
Cost
₹120–180
PROS
+
Tiny footprint for small robots
+
92% efficient, cool running
+
3.3V logic — ESP32 direct
CONS
-
13.5V max — CANNOT handle 3S LiPo!
-
1.2A tight under motor load
-
Lower startup torque
-
Single module = shared failure

## Slide 5
MOTOR COMPARISON
Best Fit
200 RPM BO + Encoder
TT gear motor · 3–6V · hall encoder
9/10
RPM
200
Voltage
3–6V
Torque
0.8 kg·cm
Encoder
Hall effect
Speed @34mm
36 cm/s
Cost
₹120–160 each
PROS
+
Ideal speed for maze navigation
+
Encoder gives precise distance
+
Fits standard BO chassis mounts
+
PWM from 3S = perfect control
CONS
-
Slightly bulky motor body
-
6V rated — use PWM at 30–40%
-
Lower torque than N20
Fast Option
300 RPM BO + Encoder
TT gear motor · 6V · hall encoder
7/10
RPM
300
Voltage
6V
Torque
0.5 kg·cm
Encoder
Hall effect
Speed @34mm
53 cm/s
Cost
₹120–160 each
PROS
+
Faster maze completion possible
+
Same encoder as 200 RPM
+
Available everywhere in India
CONS
-
Must run at 50% PWM in maze
-
Lower torque on bumps/tiles
-
More overshoot at every turn
Premium Compact
N20 Micro Gear Motor
Metal gear · 6V · optical encoder
7/10
RPM
100–200
Voltage
6V
Torque
1.5 kg·cm
Encoder
Optical/magnetic
Speed @34mm
18–35 cm/s
Cost
₹180–350 each
PROS
+
Metal gears — very durable
+
High torque in tiny body
+
Extremely precise movement
CONS
-
Expensive encoder versions
-
Custom wheel hub needed
-
Hard to source in India

## Slide 6
WHEEL COMPARISON
Best Choice
34mm Rubber Tyre
Rubber on plastic hub · BO shaft
9/10
Diameter
34 mm
@300RPM
53 cm/s
@200RPM
36 cm/s
Grip
Excellent on chart paper
Hub
Standard BO D-shaft
Cost
₹40–60 pair
PROS
+
Max grip on chart paper & plywood
+
Speed is controllable at 300 RPM
+
Encoder counts stay accurate
+
Plug-and-play BO motor hub
CONS
-
Low ground clearance
-
Picks up dust — wipe before run
-
Limited size options
Too Fast — Avoid
83mm Rubber Wheel
Large rubber tyre · adapter hub
3/10
Diameter
83 mm
@300RPM
130 cm/s !!
@200RPM
87 cm/s
Grip
Good on flat floors
Hub
Needs adapter
Cost
₹80–150 pair
PROS
+
High ground clearance
+
Smooth over tile gaps
+
Good for outdoor robots
CONS
-
130cm/s = UNCONTROLLABLE in maze
-
Must run at 25% PWM = poor control
-
Heavy — slow acceleration/braking
-
Needs hub adapter for BO shaft
-
Overshoots every 28cm turn
Budget Only
65mm Plastic Wheel
Hard plastic hub · standard BO kit
4/10
Diameter
65 mm
@300RPM
102 cm/s
@200RPM
68 cm/s
Grip
Slips on smooth surfaces
Hub
Standard BO D-shaft
Cost
₹30–50 pair
PROS
+
Cheapest available option
+
Bundled with BO motor kits
+
Consistent diameter over time
CONS
-
Slips on chart paper surface
-
102cm/s too fast for corridor
-
Encoder miscounts due to slip
-
Robot drifts sideways on turns

## Slide 7
NAVIGATION SENSOR COMPARISON
Best Value
HC-SR04 Ultrasonic
40kHz · 2–400cm · PWM echo
9/10
Range
2–400 cm
Accuracy
+/- 3 mm
Beam
~15 deg
Interface
GPIO trigger + echo
Voltage
5V (shift needed!)
Cost
₹35–50 each
PROS
+
Reliable in 28cm corridors
+
3 sensors = full wall coverage
+
₹135 total — best value
+
Huge library + tutorial support
CONS
-
5V echo damages ESP32 without shifter
-
Cross-talk if fired simultaneously
-
15 deg beam misses thin obstacles
Medium Range
Sharp GP2Y0A21 IR
Analog IR · 10–80cm · distance
5/10
Range
10–80 cm
Accuracy
+/- 5%
Output
Analog voltage
Interface
Single ADC pin
Voltage
5V
Cost
₹250–400 each
PROS
+
No cross-talk between sensors
+
Instant response time
+
Single wire per sensor
CONS
-
Expensive — ₹750 for 3 sensors
-
10cm minimum = blind spot close
-
Non-linear output needs calibration
-
Ambient IR causes false readings
Advanced Option
VL53L0X ToF Laser
I2C · 50mm–1.2m · time-of-flight
7/10
Range
50mm–1.2m
Accuracy
+/- 3%
Interface
I2C
Beam
Narrow laser
Voltage
3.3V native
Cost
₹200–350 each
PROS
+
Very narrow beam — precise
+
I2C saves GPIO pins
+
3.3V — no level shifter needed
CONS
-
50mm min = close-up blind spot
-
Black surfaces confuse readings
-
I2C address change for multiple
-
Silver tiles may cause errors

## Slide 8
COLOUR SENSOR COMPARISON
Best Choice
TCS34725
AMS · I2C · RGBC · IR filter
10/10
Interface
I2C (SDA/SCL)
IR Filter
Built-in
Clear channel
Yes (brightness)
Gain
1x to 60x
LED
White onboard
Cost
₹120–200
PROS
+
IR filter = stable under any light
+
Clear channel separates brightness
+
ONLY sensor that detects SILVER
+
60x gain for dim rooms
+
I2C saves GPIO pins
CONS
-
Mount at 6–10mm precisely
-
Slightly pricier than TCS3200
Good Backup
APDS-9960
Broadcom · I2C · RGB + proximity
7/10
Interface
I2C
IR Filter
Built-in
Bonus
Proximity + gesture
Gain
1x to 64x
LED
External needed
Cost
₹150–250
PROS
+
Proximity = bonus wall detect
+
Good black and blue detection
+
3.3V native for ESP32
CONS
-
Silver vs white unreliable
-
No onboard LED needed
-
Harder to source in India
-
Gesture wastes power
Avoid
TCS3200
AMS · PWM freq · 5V only
2/10
Interface
PWM frequency
IR Filter
None
Clear channel
No
Gain
Fixed
LEDs
4x white
Cost
₹40–80
PROS
+
Cheapest (₹40)
+
Black detection works OK
CONS
-
NO IR filter — fails under lights
-
CANNOT tell silver from white
-
5V output damages ESP32
-
PWM timing complex + slow
-
Unreliable in competition

## Slide 9
POWER SYSTEM: 3S LiPo BATTERY
3S LiPo Battery Pack
11.1V nominal · 12.6V full charge · 9.9V cutoff
Configuration
3S (3 cells in series)
Nominal voltage
11.1V
Full charge
12.6V
Low cutoff
9.9V (3.3V/cell)
Capacity
1500–2200 mAh
Discharge
20C+ recommended
Connector
XT60 / JST
Weight
~100–180g
Cost
₹500–900
PROS
+
12.6V direct to BTS7960 — max motor power
+
Light and compact for 27cm robot
POWER DISTRIBUTION
3S LiPo 12.6V
→ BTS7960 VIN
Direct — motors get full voltage
LM2596 Buck
12.6V → 5V
Powers ESP32, sensors, LED
ESP32 3.3V pin
→ TCS34725
I2C colour sensor
GPIO pins
→ Trigger/Echo
HC-SR04 ultrasonics
POWER BUDGET
2x Motors (loaded)
600 mA
ESP32 + ESP32-CAM
350 mA
HC-SR04 x3
60 mA
TCS34725 + LED + Buzz
40 mA
Total draw
~1,050 mA
Runtime (1500mAh)
~85 min

## Slide 10
CAMERA & COMPETITION OUTPUTS
ESP32-CAM MODULE
AI-Thinker · OV2640 2MP · ₹280–380
Resolution
UXGA (1600x1200)
Interface
UART serial to main ESP32
Detection
HSV colour thresholding
Mount
Face down, 8–10mm height
Use case
Blue + black zone confirm
+
Backup confirms TCS34725 readings
BLUE LED OUTPUT
5mm diffused blue LED + 100ohm resistor → ESP32 PWM pin
Rule: Blink when blue tile detected · 5 Hz · 3+ blinks minimum
ACTIVE BUZZER OUTPUT
5V active buzzer module → ESP32 digital GPIO HIGH = sound
Rule: Sound on black hazard · 500ms duration · Audible from 2m
ESSENTIAL ACCESSORIES
Logic Level Shifter x 2
₹40–70 each
HC-SR04 Echo 5V → ESP32 3.3V. Protects GPIO pins.
LM2596 Buck Converter
₹50–90
Steps 12.6V LiPo → 5V. ESP32 must never see >5V.
Perfboard + Header Pins
₹40–60
Solder final circuit. Breadboard fails under vibration.
Jumper Wires (M-M, M-F)
₹80–130
Prototyping. Get both male-male and male-female sets.

## Slide 11
COMPLETE BILL OF MATERIALS
Component
Qty
Cost
Purpose
ESP32 DevKit V1
1
₹400
Main brain controller
ESP32-CAM (AI-Thinker)
1
₹330
Tile detection camera
BTS7960 43A driver
2
₹600
Motor driver (1 per motor)
200 RPM BO motor + encoder
2
₹300
Drive motors with encoder
34mm rubber tyre pair
1
₹60
Drive wheels
25mm ball caster
1
₹60
Front support
HC-SR04 ultrasonic
3
₹135
Wall detection F/L/R
TCS34725 colour sensor
1
₹160
Tile colour detection
3S LiPo 1500mAh
1
₹600
11.1V main power
LM2596 5V buck converter
1
₹70
12.6V → 5V regulation
4-ch logic level shifter
2
₹120
5V ↔ 3.3V protection
Acrylic chassis 2-layer
1
₹280
Robot frame
M3 standoff kit
1
₹100
Frame assembly
LEDs + buzzer + wires + perf
—
₹150
Competition outputs + wiring
ESTIMATED TOTAL: ₹3,200 – ₹3,800

## Slide 12
BEST SETUP — FINAL RECOMMENDATION
BRAIN
ESP32 + ESP32-CAM
Dual core, Wi-Fi debug, camera detection
MOTOR DRIVER
BTS7960 × 2 modules
43A, 95% efficient, handles 3S LiPo 12.6V
MOTORS
300 RPM DC GEARED MOTOR
Perfect speed, 3D Printed / metal mount
WHEELS
34mm rubber tyres
Max grip on chart paper, accurate encoders
NAVIGATION
HC-SR04 × 3 (F/L/R)
₹135 total, ±3mm accuracy, wall following
COLOUR
TCS34725 (I2C)
IR filter + clear ch = black, silver, blue
POWER
3S LiPo 2200mAh + LM2596
12.6V → BTS7960 direct, 5V buck to ESP32
OUTPUTS
Blue LED + Active Buzzer
Competition required, simple GPIO, under ₹60
Total: ₹3,200–3,800 · All available in Delhi NCR · Robu.in / Amazon / Lajpat Rai

## Slide 13
BUILD SEQUENCE
1
Chassis + motors
Mount motors on acrylic, test wheel spin manually
2
BTS7960 wiring
ESP32 → BTS7960 → motors, basic forward/turn code
3
HC-SR04 × 3 mount
Front/left/right wall detection + corridor following
4
TCS34725 integration
Colour calibration for blue/black/silver on chart paper
5
ESP32-CAM setup
Mount facing down, serial to main ESP32, HSV threshold
6
LED + Buzzer wiring
Wire outputs, test blue blink + buzzer on detection
7
Full maze dry run
Build mock maze at home, test complete autonomous run
8
Competition day
Calibrate at 8 AM with actual maze → compete at 10 AM
DPS IT Fest 2026 · Rescue Maze · Navigate. Locate. Rescue.